## Slide 1: Application Templates for IPSO Smart Objects
Proposal for High Level Constructors for IPSO Smart Objects and Composite Smart Objects

## Slide 2: IPSO Smart Objects
Define simple objects like temperature sensor, load controller, accelerometer
Simple URI template of Object ID, Object Instance, Resource provides good reusability
A layer of constructor is needed to build more complex models, e.g. a thermostat or coffee maker
Also need a layer of abstraction and human-readable serialization

## Slide 3: Object Models
Typical object models are encapsulations – a thermostat contains a temperature sensor, a reference setting or set-point, and and a control output.
Need reusability and composability; a common way to build a thermostat from IPSO Temperature, Setpoint, and Control objects
Also need a way to encapsulate settings and attributes

## Slide 4: Transclusion using Object Links, like WWW
3308/0
3306/0
Thermostat
On-Off
8300 – IPSO PID Controller
3303/0 - IPSO Temperature
3308 – IPSO Setpoint
3306 – IPSO Actuation
Input
Setpoint
Output
Application
3303/0
Mode

## Slide 5: JSON Serialization
Application Templates using JSON as a high level constructor for object instances and high level composite objects
Controls object linking and encapsulation structure
Provides settings, e.g. LWM2M Observe Attributes
Provides additional core-link-format metadata for discovery
Provides semantic hooks for abstract models
Does this in a layered way as needed

## Slide 6: Example Template using Object Linking
“objects”: {
8300: {
“description”: “IPSO PID Control”,
“instances”: {
0: {
“resources”: {
7100: {
“description”: “Input Object Link”,
“value”: [3300,0]
},
7101: {
“description”: “Setpoint Object Link”,
“value”: [3308,0]
},
7102: {
“description”: “Output Object Link”,
“value”: [3306,0]
},
5750: {
“description”: ”Application Type”,
“value”: “Thermostat”
<etc>

## Slide 7
objects: {
3303: {
“description”: ”ipso temperature sensor”,
“lwm2m-attributes”: {“pmin”: 60, “pmax”: 300, “max-age”: 360},
“core-link-attributes”: {“rt”: [”oma.lwm2m”, “urn:X-ipso:temperature”]},
“instances”: {
0:{
“lwm2m-attributes”: {},
“core-link-attributes”: {“rt”: ”urn:oma:lwm2m:ext:3303”},
“resources”: {
5700:{
“description”: ”Current Measured Value”
“lwm2m-attributes”: {“pmin”: 10,”step”: 0.5},
“link-attributes”: {“rt”: ”ucum:temperature”, ”obs”, “ct”: 50}
},
5701: {
“description”: ”units”,
”value”: ”ucum:Cel”,
“operations”: [“r”]
},
5601: {“description”: ”Min Measured Value”, ”value”: 100},
5602: {“description”: ”Max Measured Value”, ”value”: 0},
5603: {“description”: ”Min Range Value”, ”value”: 0},
5604: {“description”: ”Max Range Value”, ”value”: 100},
5605: {“description”: ”Reset Min/Max”}
}
Example Template using Semantic Annotation

## Slide 8: IPSO Application Templates
Constructor for embedded objects
Constructor for complex, composite objects
Controls, e.g. LWM2M Observe Attributes
Hypermedia template for embedded server
Hypermedia template for client applications
Semantic Annotation using core-link-format metadata