## Slide 1
local
remote
1.Subscriber
2.Subscriber
2.Subscriber
Broadcast Publish
Messages
TCP connection
1.Publisher
Context
is_node
Context
is_peer
CONNECT: version |= MOSQ_NODE_MEET/local time
Context
is_peer
CONNACK: this is a peer
SUBSCRIBE: for all topics
SUBACK
PINGREQ
PINGRESP
Private Subscribe: mid/topic/qos/client id/sub id
SUBSCRIBE: from client
SUBACK
Retain PUBLISH: from node
Private Retain: topic/qos/mid/client id/sub id/ msg rcv time/payload
PUBLISH: unicast to client only
PUBLISH: from client
3.Publisher
PUBLISH: from client
PUBLISH: to whoever subscribed
PUBACK
PUBACK
Loop cycle avoidance:
For PUB msg, send to only client if this PUB comes from other nodes.
For SUB/UNSUB msg, do not broadcast if this SUB/UNSUB comes from other nodes.

## Slide 2
Implementation 1
SUB/UNSUB
Save the sub/unsub topic by ref_cnt, broardcast each sub inside Private Subscribe(slide4) msg for each new client, broadcast unsub msg for the topic which no one subscribed.
Clean Session(not implemented)
If receive a new client with clean session == 0, then broadcast it’s client id to each other node, while the client reconnect with other broker, the broker should ask it’s subs and msgs with QoS > 0 for previous broker.
QoS
Send each pub msg with it’s original QoS which specified by client to other broker,
Send each pub msg with a minus QoS between subscriber’s QoS and original QoS to real client.

## Slide 3
Implementation 2
Retain Message
Step1. (brokerA)Generate a local sub id for each sub from client,
Step2. (brokerA)Search local retain msgs and send Private Sub(slide4) msgs to other brokers
Step3. (other brokers) process the subs, and search retain msgs inside there db
Step4. (other brokers) send the retained msgs inside Private Pub(slide4) msgs to brokerA
Step5. (brokerA) cache all valid(earlier) retained msgs, send to client after 1 second
Retain msgs are tricky since there may stored on each broker.

## Slide 4
Implementation 3
PRIVATE_SUBSCRIBE
Fix head(1111 0000+Remain Length) + Packet ID + Topic Length + Topic + QoS + Original Cliend ID length + Original Client ID + Sub ID
PRIVATE_RETAIN
Fix head(1111 0000+Remain Length) + Topic Length + Topic + QoS + [Packet ID] + Original Cliend ID length + Original Client ID + Sub ID + Original Rcv Time Length + Original Retain Rcv Time + Payload
PULL_PREVIOUS_SESSION
Not implemented
SEND_PREVIOUS_SESSION
Not implemented

## Slide 5
Implementation 4
Auto reconnect
TCP connect to other nodes according the mosquitto.conf, 2s later check the TCP connection, and send CONNECT once TCP connect success, otherwise retry TCP conection 5s later.
Crash detection
For remote process crash, Kernel would close the socket,
For remote OS crash or network issue, check PINGRESP 2s later after the PINGREQ sent.
Subscribe relationship recovery
Save each topic which comes from clients, send all other nodes after CONNECT success.
Reload CFG
Try to connect with the new nodes and remove the connection with the nodes which nolonger exists in the mosquitto.conf

## Slide 6
Implementation 5
Timer optimization
Use a min heap(as libevent) to save each clients and nodes which connect with me, the key is last_msg_in + keepalive.
Simply roll poling for the context which use to connect with other nodes.
Insert the context to the min heap while accept a new socket, update the context in the socket once receive a non-DISCONNECT message, and erase the context from the heap once receive DISCONNECT message.
Use epoll_wait instead of poll, and the timeout is MIN(next_timer, 2s)
TOPIC save
Use reference counter, delete the TOPIC while this TOPIC no longer subscribed by any clients.
Deployment
Deploy one instance on one core in SMP, listen on different port.