## Slide 1: CV32E4* cores family discussion
Manuel Pezzin

## Slide 2: Current situation overview (personal point of view)
5 Official OHG projects / cores
  cv32e40pv1
  cv32e40pv2 (same repo as cv32e40pv1)
  cv32e41p (forked from cv32e40pv1)
  cv32e40x (forked from cv32e40pv1)
  cv32e40s (forked from cv32e40pv1 – sync with latest version of cv32e40x)
  cv32e40px (forked from cv32e40pv2 – sync with latest version)
Fragmented RTL/Verification code base
  Separate verification meetings
  Separate git repos for each core
  Different verification environments, hosted on independent dev branches of core-v-verif that have diverged a lot from master and even in different git repos.
  CAD tools used for design and verification ?
    Same simulators / lint / formal / etc tools ?
    Same version of Synopsys/Imperas DV ref model ?
    What about Open source CAD tools support ?
    What about SW / compiler support ?
Low coordination between OHG partners
  3/4 separate companies led 4 projects (design and verification) that address primarily their own needs
  Are these projects relevant for other end-users ?
Low involvement of academic community
  Some historical academic developers are OHG members but don’t participate directly… Did we encourage / discourage them ?
  Design/verif tools choice (commercial / signoff vs. open source ones) may be one of the reasons
Too few contributors/volunteers left to maintain such a huge and fragmented code base !
  OHG / EPFL
  CEA
  CIRRUS LOGIC
  Pascal (as an individual volunteer member, during his spare time)
  Others ?

## Slide 3: RTL code status (As far as I understand it)
cv32e40pv1
  Credits (main ones) : UNIBO/ETHZ, SILABS, OHG
  finished v1.0.0 - closed
cv32e40pv2 (same repo as cv32e40pv1)
  Credits (main ones) : DOLPHIN, OHG/EPFL, CIRRUS LOGIC, SILABS
  almost finished v1.8.3 - Orphaned
  Github public forks : 445 – 25 active over 1 year
cv32e41p (forked from cv32e40pv1)
  Credits (main ones) : OHG/EPFL/ETHZ, HUAWEI, SILABS
  Proof of concept - Closed
  Github public forks : 11 – none active
cv32e40x (forked from cv32e40pv1)
  Credits (main ones) : SILABS
  on hold v0.10.0 - Orphaned
  Github public forks : 53 - 11 active over 1 year
cv32e40s (forked from cv32e40pv1 – sync with latest version of cv32e40x)
  Credits (main ones) : SILABS
  on hold v0.10.0 - Orphaned
  Github public forks : 24 – 3 active over 1 year
cv32e40px (forked from cv32e40pv2 – sync with latest version)
  Credits (main ones) : OHG/EPFL, CEA
  Development started
  2 Active forks
    EPFL working on CV-X-IF
    CEA working on RVP extensions support
  Github public forks : 3 – 2 active over 1 year
Non-OHG versions
  Many forks maintained by academic community
  Several closed-source forks / clones used in silicon products

## Slide 4: More General thoughts
Proposed CV32E4* projects are too big and too ambitious for our (not big enough) community
   we must (re-)build an active community
   we must attract more end-users (SW / system people) to help us scheduling work in accordance with their actual short / medium / long term needs
   we must attract more industrial partners to help us on stabilization, verification and release process
   we must be more welcoming to academic community to help us on innovative / disruptive stuff
Partners come and leave
  this is normal business life  we have to manage that properly
   We should make our projects more resilient to partners departure and make life easier for newcomers / contributors
Huge feature sets means huge verification effort  delayed releases or even no release at all (when project lead leaves the boat)
Initial project goals may not be relevant after 1 or 2 years
   we should consider a divide and conquer approach : “release less, release often” model
   focus on stabilizing features rather than introducing new ones (without sacrificing innovation)
   Review/revise regularly project plans regarding targeted end-user of our work
We should think about a sustainable maintenance/support model for released cores
  Maintaining old code can be time consuming, in particular if original designers are no longer here
  Features are more important than the code itself  “upstream first” approach (make recent version backward-compatible and fix issues on recent version rather than old one)
HW features are irrelevant without proper SW support  features implementation strategy must be coordinated between HW, SW and verification (ISS / models in particular)
CVA6 development model is a source of inspiration
  Single shared RTL code base
  Proper, centralized CI(/CD?) environment
  Integration of new features is non-regression driven
  Cores are actually a set of supported configurations, verified properly

## Slide 5: Proposed new development model: initial setup
First objective: release CV32E40Pv2 (according to updated release criteria) to have a stable RTL+verif baseline
Rebuild a single git tree for RTL (and verif ?)
  Freeze existing CV32E40P/S/X/PX RTL and verif git trees
  Rebuild a new single one (CV32E4 ?) based on most stable / verified code base : a cleaned-up version of CV32E40P tree (without unmerged PULP branches) seems a good candidate
  Should we also include CV32E40X/S history (for later merge / cherry-pick of features) ?
Update existing CV32E40Pv2 verification environment for broader usage / adoption:
  Reference model: add possibility to use an alternative to Imperas-DV for broader adoption (envisioned option is spike for consistency with CVA6/CVE2 verif environments)
  Restore Verilator simulation (at least for sanity check). Commercial simulator(s) remain main option for signoff / release
  Setup a (public ?) CI/CD environment that can be duplicated locally
Create maintenance branches for (fully?) verified configurations :
  CV32E40Pv1 (should we rebrand it ?) : Basic RV32_IMC_Zicntr_Zicsr_Zifencei
    v1.0.0 is current tag
    Create maintenance branch / tag:
      v1.8.3 of CV32E40Pv2 git tree is a good candidate since they are formally equivalent (and thus backward-compatible)
      Wasn’t verified with latest version of testbench, actual functional/code coverage figures not available  we may rerun it
  CV32E40Pv2: (single brand or should we rebrand sub-configurations ?)
    Upstream GCC Floating point only (F): RV32_IMCF_Zicntr_Zicsr_Zifencei (including F0/F1/F2 pipelining configuration ?)  not part of original verif plan, should not have any coverage issue
    Upstream GCC Floating point only (FinX): RV32_IMC_Zicntr_Zicsr_Zifencei_Zfinx (including Z0/Z1/Z2 pipelining configuration ?)  not part of original verif plan, should not have any coverage issue
    Upstream GCC Core-V extensions (aka PULP): RV32_IMC_Zicntr_Zicsr_Zifencei_xcvmac_xcvalu  not part of original verif plan, should not have any coverage issue (requires disabling unused PULP features in RTL code ?)
    Full Core-V extensions (aka PULP), Core-V GCC ?: RV32_IMC_Zicntr_Zicsr_Zifencei_xcvhwlp_xcvmem_xcvmac_xcvbi_xcvalu_xcvsimd_xcvbitmanip  part of test plan (but coverage issue ?)
    PULP+F/zfinx ? (verified configs as of v1.8.3)

## Slide 6: Proposed new development model
Put in place “per-feature” short design/verif/doc/release cycles (~like agile development sprints)
  Regular meetings
    Review and sort-out issue tracker content
    (re-)schedule current and next release cycle(s)
  HW, SW and verification environment update should be performed at the same time
    Sync HW and SW schedules.
  Addressing critical issues should have higher priority than integrating new features
2 kinds of releases:
  Per-feature release tags
    Baseline : RV32_I_Zicsr_Zifencei
    Only one feature integrated (+dependencies)
     track big regression in an efficient way (shorter regression loops – idea is to trigger CI/CD only if pre-processed verilog code has changed since previous run)
  Application-oriented release tags
    Assembly of relevant feature sets for envisioned application classes  baseline for end-users
     track subtle regressions caused by interactions
Challenges:
  Find a good balance between feature inclusion and verification
  Modular documentation generation for application-oriented releases
  Probably others…

## Slide 7: Proposed short/mid term integration plan (WIP)
Split baseline CV32E40Pv1 baseline to make M and C features optional
Split PULP design config / verification to match the 8 subsets defined by GCC support
Re-integrate features from CV32E40PX/S. Priority based on increasing effort / complexity
  1/ Zmmul support  make HW divider optional
    Easy to integrate (disable HW divider)
    compiler / model / verif environment available
  2/ Initial Zc support (Zca, Zcf, Zcb)  clean replacement of C when no FPU + more base compressed instructions
    Easy to integrate (disable HW divider)
    compiler / model / verif environment available
  1/ RV32B support (Zba, Zbb , Zbc, Zbs) :
    compiler / model / verif environment available
    Integration by order of priority : 1/ Zbb – 2/ Zba – 3/ Zbs – Zbc may wait until Zbkc
  2/ RV32K support
    compiler / model / verif environment available
    1/ Zkt probably trivial on CV32E4 (only mulh and div may be data dependent)
    2/ Zbkb - 3/ Zbkx -4/ Zbkc
  3/ xcvhwlp support  to finalize CV32E40Pv2 original plan
    Solving coverage issue may take time and require HW modifications to make verification easier (design for verification)
    Upstream compiler support ?
  4/ CV-X-IF support  popular feature, requested by many end-users
    Build verification environment based on existing CVA6/CVE2 existing work
    Which implementation should we use : CV32E40X or CV32E40PX (EPFL fork) ?
    Should we integrate existing 0.1.0 support of go directly to 1.0.0 ?
  5/ Optimized multiplier
    Design done (CV32E40PX CEA fork)
    Difficult to verify and debug
  Next steps TBD

## Slide 8: Envisioned Verification configurations (WIP)
Feature verification configs (include constant time execution check, a-posteriori advertised if OK):
  Baseline : RV32_I_Zicsr_Zifencei
  Multiplication: RV32_IM_Zicsr_Zifencei, RV32_I_Zmmul_Zicsr_Zifencei
  Compressed integer: RV32_I_Zca_Zicsr_Zifencei, RV32_I_Zmmul_Zca_Zcb_Zicsr_Zifencei
  Perf counters : RV32_I_Zicsr_Zicntr_Zifencei, RV32_I_Zicsr_Zicntr_Zihpm_Zifencei
  Bitmanip : RV32_I_Zbb_Zicsr_Zifencei, RV32_I_Zba_Zicsr_Zifencei, RV32_I_Zbs_Zicsr_Zifencei
  Scalar Crypto base: RV32_I_Zbkb_Zicsr_Zifencei, RV32_I_Zbkx_Zicsr_Zifencei, RV32_I_Zbkc_Zicsr_Zifencei
  Single precision FPU : RV32_IF_Zicsr_Zifencei, RV32_I_Zfinx_Zicsr_Zifencei, RV32_IF_Zcf_Zicsr_Zifencei, RV32_I_Zfinx_Zcf_Zicsr_Zifencei
  Core-V extensions (aka PULP):
    RV32_I_Zmmul_Zicsr_Zifencei_xcvhwlp
    RV32_I_Zmmul_Zicsr_Zifencei_xcvmem
    RV32_I_Zmmul_Zicsr_Zifencei_xcvmac
    RV32_I_Zmmul_Zicsr_Zifencei_xcvbi
    RV32_I_Zmmul_Zicsr_Zifencei_xcvalu
    RV32_I_Zmmul_Zicsr_Zifencei_xcvsimd
    RV32_I_Zmmul_Zicsr_Zifencei_xcvbitmanip
  …TBD
Application-oriented verification configs (may be enriched as new features get integrated):
  Size-optimized RT microcontroller (CV32E40Pv1 tiny) : RV32_I_Zmmul_Zca_Zcb_Zicsr_Zifencei
  Profiling-enabled RT microcontroller (CV32E40Pv1) : Basic RV32_IMC_Zicntr_Zicsr_Zifencei (maybe replace C by Zca or Zca+Zcb ?)
  Floating point enabled RT microcontroller (Upstream GCC Floating point F): RV32_IMCF_Zicntr_Zicsr_Zifencei (including F0/F1/F2 pipelining config ?)
  Size-optimized Floating point enabled RT microcontroller (Upstream GCC Floating point FinX): RV32_IMC_Zfinx _Zicntr_Zicsr_Zifencei (including Z0/Z1/Z2 pipelining config ?)
  Performance-optimized RT-DSP microcontroller (Upstream GCC Core-V extensions, aka PULP): RV32_IMC_Zicntr_Zicsr_Zifencei_xcvmac_xcvalu (TBC)
  Performance-optimized RT-DSP microcontroller, fully featured (Core-V extensions, aka PULP, Core-V GCC ?): RV32_IMC_Zicntr_Zicsr_Zifencei_xcvhwlp_xcvmem_xcvmac_xcvbi_xcvalu_xcvsimd_xcvbitmanip
  … TBD

## Slide 9: Backup slides : CV32E4* features tables

## Slide 10: RISC-V Unprivileged spec support
Supported extensions | RV32I |  | RV32M |  | RV32C | Zc |  |  |  | RV32A | RV32B |  |  |  | RV32P |  |  |  | RV32K |  |  |  | RV32F | 
supported subsets | RV32I | RV32E | RV32M | Zmmul (no HW divider) | RV32C | Zca: C with the FP load/stores removed. | Zcb: simple operations. | Zcmp: push/pop and double move (overlap with c.fsdsp) | Zcmt: table jump. | RV32A | Zba: Address calculation | Zbb: Base instructions | Zbc: Carry-Less Multiply | Zbs: Bit set, Bit clear, etc. | SIMD Subset ? | Bitmanip Subset ? | Q-Format / Saturated arithmetic Subset ? | Register pair Subset ? | Zkt: Data Independent Execution Latency | Zbkc: Constant time Carry-Less Multiply | Zbkb - Bitmanip instructions for Cryptography | Zbkx: Crossbar permutations | RV32F | Zfinx
CV32E40Pv1 | 2.0 |  | 2.0 |  | 2.0 | ? |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 2.2* | v?*
CV32E40Pv2 | 2.0 |  | 2.0 |  | 2.0 | ? |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 2.2* | 1.0*
CV32E40X | 2.1 | 2.0* | 2.0 | 0.1* | 2.0 | 1.0.0 RC5.6 | 1.0.0 RC5.6 | 1.0.0 RC5.6 | 1.0.0 RC5.6 | 2.1* | 1.0.0* | 1.0.0* | 1.0.0* | 1.0.0* |  |  |  |  | 1.0.0* | 1.0.0* |  |  |  | 
CV32E40S | 2.1 | 2.0* | 2.0 | 0.1* | 2.0 | 1.0.0 RC5.6 | 1.0.0 RC5.6 | 1.0.0 RC5.6 | 1.0.0 RC5.6 | 2.1* | 1.0.0* | 1.0.0* | 1.0.0* | 1.0.0* |  |  |  |  | 1.0.0* | 1.0.0* |  |  |  | 
CV32E40PX | 2.1 |  | 2.0 |  | Zca 1.0.0 ? |  |  |  |  |  | 1.0.0* | 1.0.0* | 1.0.0* | 1.0.0* | 0.x* | 0.x* | 0.x* | 0.x* |  |  |  |  | 2.2* | 1.0*
CV32E4 | 2.1 | 2.0* | 2.0* | 1.0 | Zca+Zcf ? | 1.0.0* | 1.0.0* | 1.0.0* | 1.0.0* | 2.1* | 1.0.0* | 1.0.0* | 1.0.0* | 1.0.0* | 0.x* | 0.x* | 0.x* | 0.x* | TBD | TBD | 1.0.1* | 1.0.1* | TBD | TBD
Notes: V1/V2 configurations in blue may be verified using sequential equivalence with corresponding V2/V2 configurations (in addition to regular simulations)
V2 configurations in red will remain in RTL design but are considered for removal from verification configurations:
Low perf FP should always use ZFINX configuration
Medium/High perf FP should always use FP register file
Multicore configurations are not in PX scope
Parameters with a * may be modified to introduce fine grain modularity, to match extensions modularity (managed by compiler already)

## Slide 11: RISC-V Privileged & non-ISA spec support
Supported extensions | Privieged spec |  |  |  |  |  |  | PMP | RV DEBUG | RV CLIC
supported subsets | Zicntr: Base Counters and Timers | Zihpm: Hardware Performance Counters | Zicsr (ctrl/status reg insts) | Zifencei (instruction fetch fence) | Smstateen: State Enable Extension | U-Mode | PMA | Smepmp: PMP Enhancements for memory access and execution prevention on Machine mode | RV DEBUG | RV CLIC
CV32E40Pv1 | ? | ? | ? | ? |  |  |  |  |  | 
CV32E40Pv2 | 2.0 | ? | 2.0 | 2.0 |  |  |  |  |  | 
CV32E40X | 2.0 | 2.0 | 2.0 | 2.0 |  |  | Y | 1.0 | 1.0 | 0.9
CV32E40S | 2.0 | 2.0 | 2.0 | 2.0 | 0.6.3 | Y | Y | 1.0 | 1.0 | 
CV32E40PX | 2.0 | ? | 2.0 | 2.0 |  |  |  |  | 1.0 | TBD
CV32E4 | 2.0 | 2.0* | 2.0 | 2.0 | 1.0.0* | Y* | Y* | 1.0.0* | 1.0 | TBD
Notes: V1/V2 configurations in blue may be verified using sequential equivalence with corresponding V2/V2 configurations (in addition to regular simulations)
V2 configurations in red will remain in RTL design but are considered for removal from verification configurations:
Low perf FP should always use ZFINX configuration
Medium/High perf FP should always use FP register file
Multicore configurations are not in PX scope
Parameters with a * may be modified to introduce fine grain modularity, to match extensions modularity (managed by compiler already)

## Slide 12: CORE-V extensions/features support
Supported extensions | XCV: CORE-V PULP ISA Extensions |  |  |  |  |  |  |  | CV-X-IF | Xsecure | OBI
supported subsets | XCValu: miscellaneous ALU extension | XCVmac: multiply-accumulate | XCVelw: event load word extension | XCVbi: immediate branch | XCVmem: load/store | XCVsimd: SIMD | XCVbitmanip: Bit manipulations | XCVhwlp: Hardware loop | CV-X-IF | Xsecure: Security extensions | OBI
CV32E40Pv1 | ?* | ?* | ?* | ?* | ?* | ?* | ?* | ?* |  |  | ?
CV32E40Pv2 | 1.0* | 1.0* | 1.0* | 1.0* | 1.0* | 1.0* | 1.0* | 1.0* |  |  | 1.2
CV32E40X |  |  |  |  |  |  |  |  | 0.1* |  | 1.6.0
CV32E40S |  |  |  |  |  |  |  |  |  | 1.0 | 1.6.0
CV32E40PX | 1.0* | 1.0* | 1.0* | 1.0* | 1.0* | 1.0* | 1.0* | 1.0* | ?* |  | 
CV32E4 | 1.0* | 1.0* | 1.0* | 1.0* | 1.0* | 1.0* | 1.0* | 1.0* | 1.0* | 1.0* | 1.6.0
Notes: V1/V2 configurations in blue may be verified using sequential equivalence with corresponding V2/V2 configurations (in addition to regular simulations)
V2 configurations in red will remain in RTL design but are considered for removal from verification configurations:
Low perf FP should always use ZFINX configuration
Medium/High perf FP should always use FP register file
Multicore configurations are not in PX scope
Parameters with a * may be modified to introduce fine grain modularity, to match extensions modularity (managed by compiler already)

## Slide 13
Thank you!